## Slide 1: EECS 527 Paper Presentation
Accurate Estimation of Global Buffer Delay
Within a Floorplan
- by Charles J. Alpert, Jiang Hu, Sachin S. Sapatnekar, C.N.Sze
Presented by Yuan Zong
Department Electrical Engineering and Computer Science
University of Michigan, Ann Arbor
04/2013

## Slide 2: EECS 527 Paper Presentation
Outlines
  Introduction
  Closed-form Formula for Two-Pin Nets
        Delay Formula with No Blockages
        Delay Formula with Blockages
  Two-Pin Experiment
  Linear-Time Estimation for Trees
        Unblocked Steiner Points
        Blocked Steiner Points
        Algorithm
  Experiments for Multisink Nets
  Q & A

## Slide 3: Introduction
Closed-form expression for buffered interconnect delay
  Buffer insertion is a critical component of physical synthesis
  Previous approaches assume buffers are free to place any where
  Blockages are now first-order delay effect
  But None of the studies address the problem of delay estimation

## Slide 4: Introduction
Development on this paper
  Extension of Otten’s theory
  Predicting interconnect delays for multifanout nets in presence of blockages and validation
  A fast and simple formula is proven in real design scenarios and can be practical used in early floorplaning
  Application
      Access timing cost of different block configurations during floorplanning
      Access different Steiner routes during wire planning
      Embed the formula into a placement algorithm
Notes: Otten theory: show how one can model the blocks into a simple delay-estimation technique that applies to both two-pin and multipin nets

## Slide 5: Introduction
Key assumption in this approach
  Smaller blocks ignored
  Single-buffer type
  Block location is ignored
  Infinitesimal decoupling buffers
  Larger block front-to-end buffering
Optimally buffered line with equally spaced buffers
Optimal realizable buffering when blockages are present
Notes: Otten theory: show how one can model the blocks into a simple delay-estimation technique that applies to both two-pin and multipin nets
L-> L opt spacing btw two buffers that obtain optimal signal propagation speed. We can ignore blocks smaller than L opt. (b) is optimal realizable buffering when blockage present. As long as the blocks are smaller than Lopt, the optimal realizable buffering (b) will have a delay very close to the ideal buffering of (a).-> can assume the delay model of (a) is approximate (b).
(3) Blocks closer to source or sink has little effect on actual buffered delay.
(4) Buffers for decoupling the capacitance off the critical path can be modeled to have zero input capacitance. -> underestimation, but negligible
(5) For blocks larger than Lopt, place buffer before and after the block to assure optimal buffering.

## Slide 6: Closed-form Formula for Two-Pin Nets
Basic assumption and idea
  Assume an “ideal” buffer/inverter b that is optimal for signal propagation
  Intrinsic Resistance: Input Capacitance:
  Unit wire resistance and capacitance: R, C
  Assumption:
      Driver of net has the same drive resistance as b
      Sink of the net has an input capacitance of
      Intrinsic buffer delay is zero
= )
=

## Slide 7: Closed-form Formula for Two-Pin Nets
Delay Formula with No Blockages
  Theorem 1: The delay D(L) function of an optimally buffered line of length L with no blockages is the linear function of the design and buffer parasitic given by
    (1)
  Proof: Let k be number of stages (k-1 buffers) that result in the optimal delay along L. The length of wire between consecutive stages is L/k. The delay on the line is given by k times sum of buffer delay and wire delay
    (2)
    By taking derivative with respect to k, setting expression to zero:
    (3)

## Slide 8: Closed-form Formula for Two-Pin Nets
Delay Formula with No Blockages
  Theorem 1 is independent of number of buffers.
  Though D(L) in Equation 1 is a lower bound of realizable delay, the error is small
        As L goes to infinity, the ratio becomes one
        Maximum error occurs when k is not an integer
  Corollary 1: The optimum spacing between buffers is:
    (4)
Ratio of (1) to (2)

## Slide 9: Closed-form Formula for Two-Pin Nets
Delay Formula with Blockages
  Consider inserting a block of width w somewhere on the line L
  Let l(u,v) be the length of route from u to v
  Two cases:
        w <
          Ignore w and just use Theorem 1
        w >
          Placing a buffer before and after a blockage
          For the reset of line, use Theorem 1

## Slide 10: Closed-form Formula for Two-Pin Nets
Delay Formula with Blockages
  For w > , buffered delay is the sum of buffered delay of unblocked wires and delay needed to cross the blockage:
  (5)
  Given a set of blockages W with w > , we overload the D function in Equation 1 and ED function in Equation 5, then Blockage Buffered-Delay formula is :
  (6)
  It could conceivably overestimate delay, but the delay from an optimal solution is rarely smaller than it

## Slide 11: Two-Pin Experiment
Comparing formula D(L,W) with the optimal delay
  A single blockage
      100 nm technique
      10-mm wire
      Error is less than 1%
      Maximum error occurs at tail end
  Multiple blockages
      Different scenarios
      12-mm wire
      Error is less than 1%
A single blockage
Multiple blockages
Notes: Maximum error occurs at tail end, because this is where one may have to either inset 2 buffers that are too close together; or drive a distance that is longer than blockage.

## Slide 12: Linear-Time Estimation for Trees
Key Ideas:
  Two convenient properties of the estimation techniques
        Can be decomposed into a summation of piecewise components
        Delay can be broken into sum of delays on a given path
  T(V,E) be a Steiner tree with a source node and sinks
  RAT() be the required arrival time for sink
   quality of a buffer solution is:
  (7)
  Assumption:
        All subtrees off the critical path will be decoupled
        Decoupling buffer should have minimum possible input capacitance, assuming to be zero

## Slide 13: Linear-Time Estimation for Trees
Unblocked Steiner Points
  All decoupling of branches can be accomplished by placing the buffer near Steiner point
  Delay can be broken piecewise into sum of its subpaths
  (8)
  where D(L,W) is given by Equation 6

## Slide 14: Linear-Time Estimation for Trees
Blocked Steiner Points
  Decoupling may only occur outside the blockage
        Track the off-path capacitance and multiply it by upstream resistance
        Add the delay from extra capacitance loading on driving buffer
  represents delay from the off-path capacitance inside a blockage:
    (9)
    (10)
Notes: Since we need to insert buffer before and after blockages, we need to consider the delay of the input buffer as the delay of the blockages. R=Rb+R*lr. C=off-path cap

## Slide 15: Linear-Time Estimation for Trees
Linear-time Estimation Algorithm
  Can use Equation 10 and Equation 8 to find delay to any sink
      But how to compute the slack at source without computing each individual sink
  A linear-time algorithm to compute the slack at source
      Bottom-up tree traversal
      Edges in the tree are segmented
  Let C(v) represent subtree capacitance downstream from v
  (11)
Notes: We assume that the edges in the tree are segmented such that, whenever a blockage in W intersects a tree edge, the edge is broken into two edges incident to an intermediate boundary node (as the xis
are in Figs. 5 and 6). Therefore, each edge (u, v) lies either completely inside or outside a blockage in W. Boundary nodes lie outside W. A node lies inside W only if it is completely inside a blocking W (e.g.,
in Fig. 6 only s5 and s6 lie inside W).

## Slide 16: Linear-Time Estimation for Trees
Linear-time Estimation Algorithm
  1: visits and initializes all nodes
  2: handles cases where v is sink
  3: handles multiple children
  4: updates upstream information
  5: identifies the child of
  6: returns the slack at the source
Notes: We assume that the edges in the tree are segmented such that, whenever a blockage in W intersects a tree edge, the edge is broken into two edges incident to an intermediate boundary node (as the xis
are in Figs. 5 and 6). Therefore, each edge (u, v) lies either completely inside or outside a blockage in W. Boundary nodes lie outside W. A node lies inside W only if it is completely inside a blocking W (e.g.,
in Fig. 6 only s5 and s6 lie inside W).

## Slide 17: Experiments for Multisink Nets
Comparing 4 buffered slack calculation
  Blockage estimation in linear time (BELT): this approach
  Estimation in linear time (ELT): estimation formula while ignoring blockages
  VG1: van Ginneken’s algorithm using the single-buffer type b
  VG4: van Ginneken’s algorithm using the four types of buffer (b is the largest)

## Slide 18: Experiments for Multisink Nets
Results on Random Nets
  Comparing ELT and BELT in column 5: errors are off by over a factor of two if ignores the blockage
  Comparing BELT and VG1: underestimate by 1.1% on the average
  Comparing BELT and VG4: underestimate by 0.8% on the average

## Slide 19: Experiments for Multisink Nets
Results on Large Real Nets
  On average, ELT/BELT is 36.2%, which means blockage has a 64% impact on the average for these nets
  Impact of blockage differs: net 107 and netbig1
  On the average, error of BELT compared to VG4 is 5.2%

## Slide 20: EECS 527 Paper Presentation
Reference
  C. J. Alpert , J. Hu , S. S. Sapatnekar and C. N. Sze "Accurate estimation of global buffer delay within a floorplan", Proc. IEEE/ACM Int. Conf. Comput.-Aided Des., pp.706 -711 2004
  R. H. J. M. Otten, "Global Wires Harmful?", ACM/IEEE Intl. Symposium on Physical Design, pp. 104-109, 1998

## Slide 21: EECS 527 Paper Presentation
    Thanks!
    Q & A