## Slide 1
Impact of Local Interconnects and a Tree Growing Algorithm for Post-Grid Clock Distribution
Jiayi Xiao

## Slide 2: Paper Titles

## Slide 3: Impact of Interconnects on Timing in RLS/SDP Blocks
Local interconnects are believed to cause major impact on timing, power and routability in VLSI design
Interconnects generally affect the timing and power in the following ways
  Wire delay
  Cell delay degradation
  Slope degradation
  Delays due to the repeaters

## Slide 4: Simulation Environment
A 45nm IA processor (Nehalem)
  86 RTL-to-layout synthesis (RLS) blocks
  133 Semi-manually designed structured data
  path(SDP) blocks
Focus on the impact of local (intra-block) interconnects
  No consideration for intra-standard-cell wire delay (Poly and M1)
Source: http://www.anandtech.com/show/2658

## Slide 5: Wire Delay
The wire delay contributes to 6% and 5%, respectively, in RLS and SDP blocks
Figure 1: Wire-delay on the worst internal paths in (a) synthesized and in (b) semi-manually designed datapath blocks

## Slide 6: Cell Delay and Slope Degradation
Often known as secondary effects due to interconnects
  Not secondary anymore in nanometer technology
  It is 7% (13%) and 5% (9%) in both RLS and SDP blocks
Figure 2: Slack improvement percentage due to setting R and C of interconnects to 0 on the worst internal paths in (a) synthesized and in (b) semi-manually designed datapath blocks

## Slide 7: Repeater Count due to Interconnects
43% and 30% repeaters, respectively, in RLS and SDP blocks.
Figure 3: Number of repeaters vs. cell count in (a) synthesized and in (b) semi-manually designed datapath blocks

## Slide 8: Overall Interconnect Delay Impact Including Repeater Delays
Wires contribute to 33% and 20% of the delay in RLS and SDP blocks
  Repeaters contribute to 21% and 10%, respectively
Figure 4: Repeater delay percentage vs. slack on the worst critical paths in (a) synthesized and in (b) semi-manually designed datapath blocks

## Slide 9: Power In Clock Interconnects and Buffers for RLS Blocks
The clock trees including sequentials contribute to 70% of total dynamic power
  Only 20% of the cell count
  Clock buffers and nets contribute 16% of the dynamic power
    Only about 2% of the cell count
16%
14%
40%
Figure 5: Distribution of dynamic power in clock trees inside synthesized blocks

## Slide 10: Power In Clock Interconnects and Buffers for SDP Blocks
The clock trees including sequentials contribute to 35% of total dynamic power
  About 10% of the cell count
5%
6%
23%
Figure 6: Distribution of dynamic power in clock trees inside SDP blocks

## Slide 11: Impact to Dynamic Power in Combinational Logic for RLS Blocks
The combinational logic dissipates about 27% of the dynamic power
The repeaters (44% of cell count) constitute 30% of dynamic power
32%
68%
30%
70%
Figure 7: Distribution of dynamic power in combinational logic for synthesized blocks. (a) Distribution into combinational logic cells and interconnect. (b) Distribution of dynamic power in combinational logic cells into that in repeaters and other cells.

## Slide 12: Impact to Dynamic Power in Combinational Logic for SDP Blocks
The combinational logic dissipates about 65% of the dynamic power
The repeaters (27% of cell count) constitute 20% of dynamic power
47%
53%
20%
80%
(a)
(b)
Figure 8: Distribution of dynamic power in combinational logic for SDP blocks. (a) Distribution into combinational logic cells and interconnect. (b) Distribution of dynamic power in combinational logic cells into that in repeaters and other cells.

## Slide 13: Conclusion
Local interconnects contribute to more that 1/3 of the delay in RLS blocks and about 1/5 in SDP blocks
RLS blocks have 13% more repeater than SDP blocks
Some secondary effects are not second order
Local interconnects contribute 27% and 35% to the dynamic power in RLS and SDP blocks
  The percentage is even higher in clock trees
  Power dissipation due to clock interconnects and buffers is a big problem

## Slide 14: Routing With Constraints for Post-Grid Clock Distribution

## Slide 15: Routing With Constraints for Post-Grid Clock Distribution
In high-performance microprocessors, clocks are distributed employing hybrid networks, containing global grid followed by buffered gated trees
Figure 9: (a) Global clock distribution to layout areas employing spines for grid. (b) Clock distribution from grid wires to sequentials in a block inside layout area

## Slide 16: Routing With Constraints for Post-Grid Clock Distribution
Clock routing from global grid to buffered gated local clock tree is known as post-grid clock distribution
  Traditionally, this routing is carried out manually
  Often employing the nearest source heuristic and up-sizing strategy
    Very time-consuming and non-optimal
Figure 10: Global clock routing topology, with horizontal grid wires and tracks for routing in both directions. (b) Routing solution.

## Slide 17: Problem Formulation
A routing graph with three type nodes
  Port-nodes(), Via nodes() and Source-nodes ()
Constructing a set of trees, so that minimizing , where

## Slide 18: Tree Growing Algorithm

## Slide 19: Tree Growing Algorithm, Continued

## Slide 20: Tree Growing Algorithm, Continued

## Slide 21: Tree Growing Algorithm, Continued

## Slide 22: Tree Growing Algorithm, Continued
Figure 12: Comparison between (b) the nearest source heuristic and (c) tree-growing algorithm

## Slide 23: Algorithm Complexity and Delay Model
The time complexity of the algorithm is where are the numbers of port nodes, candidate via nodes and source nodes
The delay checking employs elmore delay model, while the skew is calculated by where is the slope of the waveform at the input of the segment

## Slide 24: Simulation Results

## Slide 25: Conclusion
Massive total wire length reduction
  14% wire length improvement compared to the nearest source heuristic
Great speed improvement
  Routing thousands of terminals over area in seconds

## Slide 26: References
[1] R. S. Shelar, “Routing With Constraints for Post-Grid Clock Distribution in Microprocessors,” IEEE Trans. Comput.-Aided Design Integr. Circuits Syst., vol 29, no. 2, pp.245-249, Feb. 2010.
[2] R. S. Shelar and M. Patyra, “Impact of Local Interconnects on Timing and Power in a High Performance Microprocessor,” in Proc. Int. Symp. Physical Design (ISPD), Mar. 2010, pp. 145-152.
[3] R. Kumar and G. Hinton. “A family of 45nm IA processors,” in International Solid-State Circuits Conference, pages 58–59, February 2009.